## Slide 1: simSCHD
Evaluation of the Static Scheduling and Timing Budget
Timur Kelin
Cambridge 2019

## Slide 2: Contents
Overview
Simulated System
Simulator Configuration and Preferences
Design Examples
References

## Slide 3: Overview

## Slide 4: Objectives
A simulation platform for the evaluation of the scheduling and timing budget.
Simplifies the initial stages of the architecture development for Hard Real Time systems.
  Allow for the simulation driven development and optimization of the architecture
Flexible, highly abstract and independent of the implementation target (HW or SW)

## Slide 5: Objectives
Input:
  Top-level timing requirements
  Outline of the processing flow
Output:
  Processing schedule and timing diagrams
  List of the execution blocks and common resources as well as the requirements for both

## Slide 6: Objectives
Benefits of using SystemC
  Short update-simulation-analysis cycle which allows for simulation driven development and optimization of the architecture
  High level of abstraction for the scheduler and execution core preferences to stay focused on the architectural tasks
  Integration into the existing simulation frameworks and workflows
  Open source

## Slide 7: Simulated System

## Slide 8: System Model
Real-Time System is simulated as a number of concurrently running Threads
Each Thread is a succession of the Tasks to execute and the Events to generate
New Thread is initiated when the specific set of the Events has been generated (Thread synchronization)
Each Task is a specification of
  Execution time,
  Set of the Execution Blocks to be occupied for the duration of the execution time, and
  Demand requested from the Common Resources by the Execution Blocks from the set.
Competition for the Execution Block is resolved by the priorities which were specified in the Thread preferences

## Slide 9: Execution Blocks and Common Resources
Each Common Resource simulates an instance which is shared by multiple Execution Blocks in the cooperative manner.
The Common Resource is characterized by its capacity
Examples
  Shared memory interface with throughput limit. Capacity: max throughput.
  Power source with the current limit. Capacity: max current.

## Slide 10: Transaction-Level Operation
At the level of elementary transactions each request from the Execution Block is granted when the Common Resource is ready to process this request.
If the Common Resource is not ready to process this request straight away, then the execution block is stalled until its request is granted.
These stalls or wait states reduce the processing performance of the Execution Block which results in the increase of the processing time.

## Slide 11: “Capacity and Demand” Model
Defining the Task execution timeframe the Execution Block demands some fraction from the capacity of the Common Resource.
If the total requested demand is less than the capacity of the Common Resource then the Execution Blocks operate at full speed.
If the total requested demand exceeds the capacity of the Common Resource then the Execution Blocks slow down. Their execution time increases to simulate stalls or wait states

## Slide 12: Simulation of the Capacity Exceeding
If the total requested demand exceeds the capacity of the Common Resource then the execution time of the Tasks, which use this Common Resource, increases.
  All the Execution Blocks, which are involved in the execution of these Tasks, slow down.
  Total demand from the Execution Blocks operating at lower speed doesn’t exceed the capacity of the Common Resource.
  The slowdown decreases the demand requested from other Common Resources

## Slide 13: Block Diagram of the Simulation Platform

## Slide 14: Planner
Executes multiple concurrent Threads
Keeps the register of the Events generated by the running Threads
  Events are used for the synchronization between the Threads
Assigns the available Execution Blocks to the Tasks which are called by the running Threads
  Resolves Thread priorities
Transmits runtime configuration to the Execution Blocks and receives their state
  Keeps the record of the available and busy Execution Blocks

## Slide 15: Execution Block
Receives runtime configuration from the Planner
Transmits requests with the demand values to the Common Resources
Receives the information from the Common Resource about its total demand, combines the information from the multiple Common Resources and adjusts the execution time accordingly
Transmits “available” status to the Planner when the execution time is expired

## Slide 16: Common Resource
Receives requests with the demand values from the Execution Blocks
Calculates total demand requested by all of the Execution Blocks which are using this Resource
Broadcasts the value of the total demand to all of the Execution Blocks which are using this Resource

## Slide 17: Simulator Configuration and Preferences

## Slide 18: Simulator Preferences
Preferences are supplied to the simulator via the JSON file specified as a single command line parameter

## Slide 19: Top-level JSON Fields
“threads”: an array of thread specifications
“tasks”: an array of task specifications
“executors”: an array of the names of the execution blocks available in the system
“common”: an array of common resource specifications
“time”: specification of the simulation time and resolution
“trace”: specification of the VCD trace and waveform translation
“dump”: an array of data dump specifications for the different points of the simulated system
“report”: controls for SystemC logging and reporting
Please refer to the examples for the specification details

## Slide 20: Thread Specification
“name”: name of the thread. It is used in the in the VCD trace map.
“priority”: numeric value which is used to allocate execution blocks in the case of competition.
“start”: array of the regex-es which correspond to the event names. All the events from the list should occur for the thread to start (and-list).
  To restart the thread the new set of the events should occur.
  __start__ is the name of the event which corresponds to the start of the simulation

## Slide 21: Thread Specification
“sequence”: array of the tasks and events. The tasks are executed and the events are generated in the order of their appearance in the array.
  “task”: specifies task parameters
    “run”: name of the task to execute
    “param”: task parameters for VCD trace map
  “event”: name of the event to be generated. It is resolved in the “start” list of a thread.
  “sequence” should start with a “task” specification
  2 or more “event” specifications one right after another are not allowed

## Slide 22: Task Specification
“name”: name of the task. The task is called by its name from the “sequence” array of a thread.
“exec”: array of the parameters specified for the execution blocks which are involved in the task execution. Each element of the array specifies:
  “run”: name regex of the execution block
  “use”: array of the parameters of the common resources. Each element of the array specifies:
    “res”: name of the common resource which is addressed by the execution block
    “demand”: demand from the common resource
  “opt”: options which are passed to the execution block in the co-simulation environment

## Slide 23: Task Specification
“runtime”: time of the task execution.
  This time is specified in the assumption that the total demand from the common resources, which are specified in the “use” array of the “exec” elements, doesn’t exceed their capacity within the timeframe of the execution.
  In other words “runtime” is specified without the effect of common resources been taken into account.
  During the simulation the time for which the execution blocks are occupied can be different from the one specified in the “runtime” field

## Slide 24: Execution Block Specification
“name”: name of the execution block. It is addressed in the “run” fields of the task specification

## Slide 25: Common Resource Specification
“name”: name of the common resource.
“capacity”: capacity of the common resource.

## Slide 26: Time Specification
“resolution”: specifies simulation time resolution. See [3] section 5.11.3
“finish”: specifies simulation time. See [3] section 4.3.4.2

## Slide 27: VCD Trace Specification

## Slide 28: Data Dump Specification

## Slide 29: Logging and Reporting Specification

## Slide 30: Design Examples

## Slide 31: References

## Slide 32: Source Code and Documentation
[1] Simulation Framework for the Static Scheduler:
  https://github.com/timurkelin/simschd
[2] simSCHD and simSIMD Co-simulation environment:
  https://github.com/timurkelin/cosim
[3] IEEE Std 1666-2011, IEEE Standard for Standard SystemC Language Reference Manual